| XXIV MEETING OF PERMANENT CONSULTATIVE COMMITTEE II: RADIOCOMMUNICATIONS September 29 to October 3, 2014 Mérida City, Yucatán, México | OEA/Ser.L/XVII.4.2 CCP.II-RADIO/doc. 3694/14 1 October 2014 Original: English |
| --- | --- |
|  | AGENDA ITEM 1.17: INTER-AMERICAN PROPOSAL FOR WRC-15 |  |
|  | (Item on the Agenda: 3.1 (SGT2)) |  |
|  | (Document submitted by the Coordinator) |  |

SGT 2 – Radiolocation, Amateur, Maritime, and Aeronautical issues

Coordinator: Mr. Jonathan WILLIAMS, UNITED STATES OF AMERICA (jwilliams@ntia.doc.gov)

Alternate Coordinator: Mr. Javier GARCIA, DOMINICAN REPUBLIC (jgarcia@indotel.gob.do)

Rapporteur Agenda Item: Ms Marcella OST,  CANADA (marcella.s.ost@boeing.com)

Alternate Rapporteur Agenda Item: Luiz Fernando de SOUZA, BRAZIL (lfsouza@embraer.com.br)

Agenda Item 1.17:  to consider possible spectrum requirements and regulatory actions, including appropriate aeronautical allocations, to support wireless avionics intra-communications (WAIC), in accordance with Resolution 423 (WRC-12)

Background:

B [doc 3431r1]

The aerospace industry is developing the future generation of commercial aircraft to provide airlines and the flying public more cost-efficient, safe, and reliable aircraft. Wireless capabilities will reduce aircraft weight, provide multiple and redundant methods to transmit safety-related information, and provide environmental benefits and cost savings to manufacturers and operators.

WAIC systems consist of multiple radiocommunication devices between two or more transmitters and receivers on a single aircraft and provide safety-related aircraft applications. WAIC system transmissions are located both inside and outside the aircraft with the majority being interior to the aircraft structure.

WAIC communication traffic will be between transmitters and receivers on the same aircraft as part of a closed, exclusive network required for aircraft operation.  WAIC systems will not provide air-to-ground, air-to-air or air-to-satellite communications.

USA [doc 3467]

The 2012 World Radiocommunication Conference (WRC-12) in response to a request to consider possible spectrum requirements and regulatory measures in support of wireless avionics communication systems approved Agenda Item 1.17 for WRC-15.

WRC-12 resolved to invite the ITU-R to consider, based on the results of ITU-R studies, possible regulatory actions, including appropriate aeronautical allocations, to support the implementation of WAIC systems, while taking into account spectrum requirements for WAIC and protection requirements for incumbent systems operating in accordance with existing allocations.

Resolution 423 (WRC-12) invites Working Party 5B (WP5B) to consider:

- frequency bands within existing worldwide aeronautical mobile service, aeronautical mobile (R) service and aeronautical radionavigation service allocations; and

- additional frequency bands above 15.7 GHz for aeronautical services if spectrum requirements cannot be met in frequency bands studied under invites ITU-R 3 i)

Studies submitted to WP5B show that WAIC systems can be accommodated in the band 4200-4400 MHz provided that mitigation techniques for some applications, provided in [Working document towards a preliminary draft new Report, ITU-R M.[WAIC_SHARING_4 200-4 400MHz - Compatibility analysis between wireless avionics intra-communications systems and systems in the existing services in the frequency band 4 200-4 400 MHz.  Document 5B/TEMP/241] are utilized.  If such mitigation techniques cannot be utilized, then some external WAIC applications might not be compatible with existing aeronautical services.

However, both radio altimeter and WAIC systems are aeronautical applications and regulated by aviation certification authorities.  Additional standardization and aircraft certification efforts must occur within the aviation community in order to guarantee the safe and compatible operation of WAIC and radio altimeter systems.

Proposal:

MOD       IAP/1.17/1

Support:

Brazil (Federative Republic of), Canada, Dominican Republic, Ecuador, El Salvador (Republic of), Guatemala (Republic of), United States of America, Uruguay (Eastern Republic of), Nicaragua

[Antigua and Barbuda], [Argentine Republic], [Bahamas (Commonwealth of the)], [Barbados], [Belize], [Bolivia (Plurinational State of)],   [Chile], [Colombia (Republic of)], [Costa Rica], [Dominica (Commonwealth of)],     [Grenada],  [Guyana], [Haiti (Republic of)], [Honduras (Republic of)], [Jamaica], [Mexico],  [Panama (Republic of)], [Paraguay (Republic of)], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis (Federation of)], [Suriname (Republic of)], [Trinidad and Tobago], [Venezuela (Bolivarian Republic of)]

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations

4 200-4 400 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 4 200-4 400 AERONAUTICAL RADIONAVIGATION MOD 5.438 AERONAUTICAL MOBILE (R) ADD 5.XXX 5.4395.440 ADD 5.YYY |

MOD	IAP/1.17/2

Support:

Brazil (Federative Republic of), Canada, Dominican Republic, Ecuador, El Salvador (Republic of), Guatemala (Republic of), United States of America, Uruguay (Eastern Republic of), Nicaragua

[Antigua and Barbuda], [Argentine Republic], [Bahamas (Commonwealth of the)], [Barbados], [Belize], [Bolivia (Plurinational State of)],   [Chile], [Colombia (Republic of)], [Costa Rica], [Dominica (Commonwealth of)],     [Grenada],  [Guyana], [Haiti (Republic of)], [Honduras (Republic of)], [Jamaica], [Mexico],  [Panama (Republic of)], [Paraguay (Republic of)], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis (Federation of)], [Suriname (Republic of)], [Trinidad and Tobago], [Venezuela (Bolivarian Republic of)]

5.438	Use of the band 4 200-4 400 MHz by the aeronautical radionavigation service is reserved exclusively for radio altimeters installed on board aircraft and for the associated transponders on the ground.

ADD 	IAP/1.17/3

Support:

Brazil (Federative Republic of), Canada, Dominican Republic, Ecuador, El Salvador (Republic of), Guatemala (Republic of), United States of America, Uruguay (Eastern Republic of), Nicaragua

[Antigua and Barbuda], [Argentine Republic], [Bahamas (Commonwealth of the)], [Barbados], [Belize], [Bolivia (Plurinational State of)],   [Chile], [Colombia (Republic of)], [Costa Rica], [Dominica (Commonwealth of)],     [Grenada],  [Guyana], [Haiti (Republic of)], [Honduras (Republic of)], [Jamaica], [Mexico],  [Panama (Republic of)], [Paraguay (Republic of)], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis (Federation of)], [Suriname (Republic of)], [Trinidad and Tobago],  [Venezuela (Bolivarian Republic of)]

5.XXX	Use of the frequency band 4 200- 4 400 MHz by the aeronautical mobile (R) service is limited to internationally standardized aeronautical systems for the provision of wireless avionics intra-communications.

5.YYY	Passive sensing in the Earth exploration-satellite and space research services may be authorized in the band 4200-4400 MHz on a secondary basis (no protection is provided by radio altimeters or by wireless avionics intra-communications).

Reason:  To add a primary Aeronautical mobile (route) service (AM(R)S) allocation in the frequency band 4200-4400 MHz to Article 5 of the Radio Regulations.  The AM(R)S allocation is limited to WAIC systems via footnote.  The Earth exploration-satellite and Space research services maintain their status via footnote.

SUP	IAP/1.17/4

Support:

Brazil (Federative Republic of), Canada, Dominican Republic, Ecuador, El Salvador (Republic of), Guatemala (Republic of), United States of America, Uruguay (Eastern Republic of), Nicaragua

[Antigua and Barbuda], [Argentine Republic], [Bahamas (Commonwealth of the)], [Barbados], [Belize], [Bolivia (Plurinational State of)],   [Chile], [Colombia (Republic of)], [Costa Rica], [Dominica (Commonwealth of)],     [Grenada],  [Guyana], [Haiti (Republic of)], [Honduras (Republic of)], [Jamaica], [Mexico],  [Panama (Republic of)], [Paraguay (Republic of)], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis (Federation of)], [Suriname (Republic of)], [Trinidad and Tobago],  [Venezuela (Bolivarian Republic of)]

RESOLUTION 423 (WRC-12)

Consideration of regulatory actions, including allocations, to support
Wireless Avionics Intra-Communications

Reason:  The required studies have been completed and this resolution is no longer needed.

_____________